## Slide 1: William Stallings, Computer Organization and Architecture,9th Edition
Chapter 3
A Top-Level View of Computer
Function and Interconnection
Notes: Lecture slides prepared for “Computer Organization and Architecture”, 9/e, by William Stallings, Chapter 3 “A Top Level View of Computer Function and Interconnection”.
Adapted by Thân Văn Sử

## Slide 2: Objectives
At top level, what are main components of a computer?
How are they connected?
After studying this chapter, you should be able to:
  Understand the basic elements of an instruction cycle and the role of interrupts.
  Describe the concept of interconnection within a computer system.
  Understand the difference between synchronous and asynchronous bus timing.
  Explain the need for multiple buses arranged in a hierarchy.
  Assess the relative advantages of point-to-point interconnection compared to bus interconnection.
Notes: As discussed in Chapter 2, virtually all contemporary computer designs are based
on concepts developed by John von Neumann at the Institute for Advanced Studies,
Princeton. Such a design is referred to as the von Neumann architecture and is based
on three key concepts:
• Data and instructions are stored in a single read–write memory.
• The contents of this memory are addressable by location, without regard to
the type of data contained there.
• Execution occurs in a sequential fashion (unless explicitly modified) from one
instruction to the next.
The reasoning behind these concepts was discussed in Chapter 2 but is worth
summarizing here. There is a small set of basic logic components that can be
combined in various ways to store binary data and perform arithmetic and logical
operations on that data. If there is a particular computation to be performed, a
configuration of logic components designed specifically for that computation could
be constructed. We can think of the process of connecting the various components
in the desired configuration as a form of programming. The resulting “program” is
in the form of hardware and is termed a hardwired program.

## Slide 3: Contents
3.1- Computer Components
3.2- Computer Function
3.3- Interconnection Structures
3.4- Bus Interconnection
Notes: As discussed in Chapter 2, virtually all contemporary computer designs are based
on concepts developed by John von Neumann at the Institute for Advanced Studies,
Princeton. Such a design is referred to as the von Neumann architecture and is based
on three key concepts:
• Data and instructions are stored in a single read–write memory.
• The contents of this memory are addressable by location, without regard to
the type of data contained there.
• Execution occurs in a sequential fashion (unless explicitly modified) from one
instruction to the next.
The reasoning behind these concepts was discussed in Chapter 2 but is worth
summarizing here. There is a small set of basic logic components that can be
combined in various ways to store binary data and perform arithmetic and logical
operations on that data. If there is a particular computation to be performed, a
configuration of logic components designed specifically for that computation could
be constructed. We can think of the process of connecting the various components
in the desired configuration as a form of programming. The resulting “program” is
in the form of hardware and is termed a hardwired program.

## Slide 4: 3.1- Computer Components
Contemporary (nowaday) computer designs are based on concepts developed by John von Neumann at the Institute for Advanced Studies, Princeton
Referred to as the von Neumann architecture and is based on three key concepts:
  Data and instructions are stored in a single read-write memory
  The contents of this memory are addressable by location, without regard to the type of data contained there
  Execution occurs in a sequential fashion (unless explicitly modified) from one instruction to the next
  Hardwired program
  The result of the process of connecting the various components in the desired configuration
Notes: As discussed in Chapter 2, virtually all contemporary computer designs are based
on concepts developed by John von Neumann at the Institute for Advanced Studies,
Princeton. Such a design is referred to as the von Neumann architecture and is based
on three key concepts:
• Data and instructions are stored in a single read–write memory.
• The contents of this memory are addressable by location, without regard to
the type of data contained there.
• Execution occurs in a sequential fashion (unless explicitly modified) from one
instruction to the next.
The reasoning behind these concepts was discussed in Chapter 2 but is worth
summarizing here. There is a small set of basic logic components that can be
combined in various ways to store binary data and perform arithmetic and logical
operations on that data. If there is a particular computation to be performed, a
configuration of logic components designed specifically for that computation could
be constructed. We can think of the process of connecting the various components
in the desired configuration as a form of programming. The resulting “program” is
in the form of hardware and is termed a hardwired program.

## Slide 5: Hardware and Software Approaches
Notes: Now consider this alternative. Suppose we construct a general-purpose
configuration of arithmetic and logic functions. This set of hardware will perform
various functions on data depending on control signals applied to the hardware.
In the original case of customized hardware, the system accepts data and produces
results (Figure 3.1a). With general-purpose hardware, the system accepts data and
control signals and produces results. Thus, instead of rewiring the hardware for each
new program, the programmer merely needs to supply a new set of control signals.
How shall control signals be supplied? The answer is simple but subtle. The
entire program is actually a sequence of steps. At each step, some arithmetic or
logical operation is performed on some data. For each step, a new set of control
signals is needed. Let us provide a unique code for each possible set of control
signals, and let us add to the general-purpose hardware a segment that can accept a
code and generate control signals (Figure 3.1b).

## Slide 6: I/O Components
Software
A sequence of codes or instructions
Part of the hardware interprets each instruction and generates control signals
Provide a new sequence of codes for each new program instead of rewiring the hardware
Major components:
Means of reporting results
Output module
Contains basic components for accepting data and instructions and converting them into an internal form of signals usable by the system
Input module
I/O Components
Module of general-purpose arithmetic and logic functions
Instruction interpreter
CPU
Software
Notes: Programming is now much easier. Instead of rewiring the hardware for each
new program, all we need to do is provide a new sequence of codes. Each code
is, in effect, an instruction, and part of the hardware interprets each instruction
and generates control signals. To distinguish this new method of programming, a
sequence of codes or instructions is called software.
Figure 3.1b indicates two major components of the system: an instruction
interpreter and a module of general-purpose arithmetic and logic functions. These
two constitute the CPU. Several other components are needed to yield a functioning
computer. Data and instructions must be put into the system. For this we need some
sort of input module. This module contains basic components for accepting data
and instructions in some form and converting them into an internal form of signals
usable by the system. A means of reporting results is needed, and this is in the form
of an output module. Taken together, these are referred to as I/O components.

## Slide 7: MEMORY
Memory address register (MAR)
Specifies the address in memory for the next read or write
Memory buffer register (MBR)
Contains the data to be written into memory or receives the data read from memory
I/O address register (I/OAR)
Specifies a particular I/O device
I/O buffer register (I/OBR)
Used for the exchange of data between an I/O module and the CPU
MAR
MBR
Notes: One more component is needed. An input device will bring instructions and
data in sequentially. But a program is not invariably executed sequentially; it may
jump around (e.g., the IAS jump instruction). Similarly, operations on data may
require access to more than just one element at a time in a predetermined sequence.
Thus, there must be a place to store temporarily both instructions and data. That
module is called memory, or main memory, to distinguish it from external storage or
peripheral devices. Von Neumann pointed out that the same memory could be used
to store both instructions and data.
The CPU exchanges data with memory. For this purpose, it typically
makes use of two internal (to the CPU) registers: a memory address register (MAR),
which specifies the address in memory for the next read or write, and a memory
buffer register (MBR), which contains the data to be written into memory or receives
the data read from memory. Similarly, an I/O address register (I/OAR) specifies a
particular I/O device. An I/O buffer (I/OBR) register is used for the exchange of
data between an I/O module and the CPU.

## Slide 8: Computer Components: Top Level View
Notes: Figure 3.2 illustrates these top-level components and suggests the interactions
among them.
A memory module consists of a set of locations, defined by sequentially
numbered addresses. Each location contains a binary number that can be interpreted
as either an instruction or data. An I/O module transfers data from external devices
to CPU and memory, and vice versa. It contains internal buffers for temporarily
holding these data until they can be sent on.

## Slide 9: 3.2- Computer Function
Basic Instruction Cycle
Notes: In its simplest form, instruction processing
consists of two steps: The processor reads (fetches) instructions from memory one
at a time and executes each instruction. Program execution consists of repeating the
process of instruction fetch and instruction execution. The instruction execution may
involve several operations and depends on the nature of the instruction.
The processing required for a single instruction is called an instruction cycle.
Using the simplified two-step description given previously, the instruction cycle is
depicted in Figure 3.3. The two steps are referred to as the fetch cycle and the execute
cycle. Program execution halts only if the machine is turned off, some sort of unrecoverable
error occurs, or a program instruction that halts the computer is encountered.

## Slide 10: Fetch Cycle
At the beginning of each instruction cycle the processor fetches an instruction from memory
  The program counter (PC) holds the address of the instruction to be fetched next
  The processor increments the PC after each instruction fetch so that it will fetch the next instruction in sequence
The fetched instruction is loaded into the instruction register (IR)
  The processor interprets the instruction and performs the required action
Notes: At the beginning of each instruction cycle, the processor fetches an instruction
from memory. In a typical processor, a register called the program counter (PC)
holds the address of the instruction to be fetched next. Unless told otherwise, the
processor always increments the PC after each instruction fetch so that it will fetch
the next instruction in sequence (i.e., the instruction located at the next higher memory
address). So, for example, consider a computer in which each instruction occupies
one 16-bit word of memory. Assume that the program counter is set to memory
location 300, where the location address refers to a 16-bit word. The processor will
next fetch the instruction at location 300. On succeeding instruction cycles, it will
fetch instructions from locations 301, 302, 303, and so on. This sequence may be
altered, as explained presently.
The fetched instruction is loaded into a register in the processor known as
the instruction register (IR). The instruction contains bits that specify the action
the processor is to take. The processor interprets the instruction and performs the
required action.

## Slide 11: Action Categories of actions
Processor-memory
Data transferred from processor to memory or from memory to processor
Processor-I/O
Data transferred to or from a peripheral device by transferring between the processor and an
Data processing
The processor may perform some arithmetic or logic operation on data
Control
An instruction may specify that the sequence of execution be altered
I/O module
Notes: In general, these actions fall into four categories:
Processor-memory: Data may be transferred from processor to memory or
from memory to processor.
• Processor-I/O: Data may be transferred to or from a peripheral device by
transferring between the processor and an I/O module.
• Data processing: The processor may perform some arithmetic or logic operation
on data.
• Control: An instruction may specify that the sequence of execution be altered.
For example, the processor may fetch an instruction from location 149, which
specifies that the next instruction be from location 182. The processor will
remember this fact by setting the program counter to 182. Thus, on the next
fetch cycle, the instruction will be fetched from location 182 rather than 150.
An instruction’s execution may involve a combination of these actions.

## Slide 12: Instruction structure:
Máy giả định
Opcode 4 bits  16 actions
Notes: Consider a simple example using a hypothetical machine that includes the
characteristics listed in Figure 3.4. The processor contains a single data register,
called an accumulator (AC). Both instructions and data are 16 bits long. Thus, it is
convenient to organize memory using 16-bit words. The instruction format provides
4 bits for the opcode, so that there can be as many as 24 = 16 different opcodes, and
up to 212 = 4096 (4K) words of memory can be directly addressed.

## Slide 13: Example of Program Execution
1940(h)
1(h): 0001
 Load AC from memory 940(h)
5941(h)
5(h) 0101
 Add to AC from memory 941(h)
2941(h)
2(h): 0010Store AC to memory 941
 Add 2 memory cell at addresses 940, 941. The result is stored at 941
Notes: Figure 3.5 illustrates a partial program execution, showing the relevant
portions of memory and processor registers. The program fragment shown adds
the contents of the memory word at address 940 to the contents of the memory
word at address 941 and stores the result in the latter location. Three instructions,
which can be described as three fetch and three execute cycles, are required:
1. The PC contains 300, the address of the first instruction. This instruction (the
value 1940 in hexadecimal) is loaded into the instruction register IR, and
the PC is incremented. Note that this process involves the use of a memory
address register and a memory buffer register. For simplicity, these intermediate
registers are ignored.
2. The first 4 bits (first hexadecimal digit) in the IR indicate that the AC is to be
loaded. The remaining 12 bits (three hexadecimal digits) specify the address
(940) from which data are to be loaded.
3. The next instruction (5941) is fetched from location 301, and the PC is
incremented.
4. The old contents of the AC and the contents of location 941 are added, and
the result is stored in the AC.
5. The next instruction (2941) is fetched from location 302, and the PC is
incremented.
6. The contents of the AC are stored in location 941.
In this example, three instruction cycles, each consisting of a fetch cycle and an
execute cycle, are needed to add the contents of location 940 to the contents of 941.
With a more complex set of instructions, fewer cycles would be needed. Some older
processors, for example, included instructions that contain more than one memory
address. Thus, the execution cycle for a particular instruction on such processors could
involve more than one reference to memory. Also, instead of memory references, an
instruction may specify an I/O operation.

## Slide 14: Instruction Cycle State Diagram
Notes: Vị trí khởi đầu luôn nằm trái dưới
The execution cycle for a particular instruction may involve more than one
reference to memory. Also, instead of memory references, an instruction may specify
an I/O operation. With these additional considerations in mind, Figure 3.6 provides
a more detailed look at the basic instruction cycle of Figure 3.3. The figure is in the
form of a state diagram.
For any given instruction cycle, some states may be null and
others may be visited more than once. The states can be described as follows:
• Instruction address calculation (iac): Determine the address of the next
instruction to be executed. Usually, this involves adding a fixed number to
the address of the previous instruction. For example, if each instruction is 16
bits long and memory is organized into 16-bit words, then add 1 to the previous
address. If, instead, memory is organized as individually addressable 8-bit
bytes, then add 2 to the previous address.
• Instruction fetch (if): Read instruction from its memory location into the
processor.
• Instruction operation decoding (iod): Analyze instruction to determine type
of operation to be performed and operand(s) to be used.
• Operand address calculation (oac): If the operation involves reference to an
operand in memory or available via I/O, then determine the address of the
operand.
• Operand fetch (of): Fetch the operand from memory or read it in from I/O.
• Data operation (do): Perform the operation indicated in the instruction.
• Operand store (os): Write the result into memory or out to I/O.
States in the upper part of Figure 3.6 involve an exchange between the
processor and either memory or an I/O module. States in the lower part of the
diagram involve only internal processor operations. The oac state appears twice,
because an instruction may involve a read, a write, or both. However, the action performed
during that state is fundamentally the same in both cases, and so only a single
state identifier is needed.
Also note that the diagram allows for multiple operands and multiple results,
because some instructions on some machines require this. For example, the PDP-11
instruction ADD A,B results in the following sequence of states: iac, if, iod, oac, of,
oac, of, do, oac, os.
Finally, on some machines, a single instruction can specify an operation to be performed
on a vector (one-dimensional array) of numbers or a string (one-dimensional
array) of characters. As Figure 3.6 indicates, this would involve repetitive operand fetch
and/or store operations.

## Slide 15: Classes of Interrupts
Virtually all computers provide a mechanism by which other modules (I/O, memory) may interrupt the normal processing of the processor. An interrupt can be caused by:
CPU
IO Module
5V
Notes: Ngắt là tín hiệu của I/O thông báo cho CPU biết rằng nó sẵn sàng
Virtually all computers provide a mechanism by which other modules (I/O, memory)
may interrupt the normal processing of the processor. Table 3.1 lists the most common
classes of interrupts. The specific nature of these interrupts is examined
later in this book, especially in Chapters 7 and 14. However, we need to introduce the concept
now to understand more clearly the nature of the instruction cycle and the implications
of interrupts on the interconnection structure.

## Slide 16: Program Flow Control
Read keyboard
Notes: Interrupts are provided primarily as a way to improve processing efficiency.
For example, most external devices are much slower than the processor. Suppose
that the processor is transferring data to a printer using the instruction cycle scheme
of Figure 3.3. After each write operation, the processor must pause and remain
idle until the printer catches up. The length of this pause may be on the order of
many hundreds or even thousands of instruction cycles that do not involve memory.
Clearly, this is a very wasteful use of the processor.
Figure 3.7a illustrates this state of affairs. The user program performs a series
of WRITE calls interleaved with processing. Code segments 1, 2, and 3 refer to
sequences of instructions that do not involve I/O. The WRITE calls are to an I/O
program that is a system utility and that will perform the actual I/O operation. The
I/O program consists of three sections:
• A sequence of instructions, labeled 4 in the figure, to prepare for the actual
I/O operation. This may include copying the data to be output into a special
buffer and preparing the parameters for a device command.
• The actual I/O command. Without the use of interrupts, once this command is
issued, the program must wait for the I/O device to perform the requested function
(or periodically poll the device). The program might wait by simply repeatedly
performing a test operation to determine if the I/O operation is done.
• A sequence of instructions, labeled 5 in the figure, to complete the operation.
This may include setting a flag indicating the success or failure of the operation.
Because the I/O operation may take a relatively long time to complete, the I/O
program is hung up waiting for the operation to complete; hence, the user program
is stopped at the point of the WRITE call for some considerable period of time.
With interrupts, the processor can
be engaged in executing other instructions while an I/O operation is in progress.
Consider the flow of control in Figure 3.7b. As before, the user program reaches a
point at which it makes a system call in the form of a WRITE call. The I/O program
that is invoked in this case consists only of the preparation code and the actual I/O
command. After these few instructions have been executed, control returns to the
user program. Meanwhile, the external device is busy accepting data from computer
memory and printing it. This I/O operation is conducted concurrently with the
execution of instructions in the user program.
When the external device becomes ready to be serviced—that is, when it is
ready to accept more data from the processor—the I/O module for that external
device sends an interrupt request signal to the processor. The processor responds by
suspending operation of the current program, branching off to a program to service
that particular I/O device, known as an interrupt handler, and resuming the original
execution after the device is serviced. The points at which such interrupts occur are
indicated by an asterisk in Figure 3.7b.
Let us try to clarify what is happening in Figure 3.7. We have a user program
that contains two WRITE commands. There is a segment of code at the beginning,
then one WRITE command, then a second segment of code, then a second WRITE
command, then a third and final segment of code. The WRITE command invokes the
I/O program provided by the OS. Similarly, the I/O program consists of a segment
of code, followed by an I/O command, followed by another segment of code. The I/O
command invokes a hardware I/O operation.

## Slide 17: Transfer of Control via Interrupts
A controls B means that B must perform all instructions from A.
Hardware must perform actions specified in each instruction
Proccess controls hardware
Notes: From the point of view of the user program, an interrupt is just that: an interruption
of the normal sequence of execution. When the interrupt processing is completed,
execution resumes (Figure 3.8). Thus, the user program does not have to contain any
special code to accommodate interrupts; the processor and the operating system are
responsible for suspending the user program and then resuming it at the same point.

## Slide 18: Instruction Cycle With Interrupts
CPU
IO Module
5V
OS decides whether CPU accepts interrupt or not
Notes: To accommodate interrupts, an interrupt cycle is added to the instruction
cycle, as shown in Figure 3.9. In the interrupt cycle, the processor checks to see if
any interrupts have occurred, indicated by the presence of an interrupt signal. If no
interrupts are pending, the processor proceeds to the fetch cycle and fetches the
next instruction of the current program. If an interrupt is pending, the processor
does the following:
• It suspends execution of the current program being executed and saves its
context. This means saving the address of the next instruction to be executed
(current contents of the program counter) and any other data relevant to the
processor’s current activity.
• It sets the program counter to the starting address of an interrupt handler routine.
The processor now proceeds to the fetch cycle and fetches the first instruction
in the interrupt handler program, which will service the interrupt. The interrupt
handler program is generally part of the operating system. Typically, this program
determines the nature of the interrupt and performs whatever actions are needed.
In the example we have been using, the handler determines which I/O module
generated the interrupt and may branch to a program that will write more data out
to that I/O module. When the interrupt handler routine is completed, the processor
can resume execution of the user program at the point of interruption.
It is clear that there is some overhead involved in this process. Extra instructions
must be executed (in the interrupt handler) to determine the nature of the interrupt
and to decide on the appropriate action. Nevertheless, because of the relatively large
amount of time that would be wasted by simply waiting on an I/O operation, the
processor can be employed much more efficiently with the use of interrupts.

## Slide 19: Program Timing: Short I/O Wait
Notes: To appreciate the gain in efficiency, consider Figure 3.10, which is a timing diagram
based on the flow of control in Figures 3.7a and 3.7b. In this figure, user program
code segments are shaded green, and I/O program code segments are shaded
gray. Figure 3.10a shows the case in which interrupts are not used. The processor must
wait while an I/O operation is performed.
Figures 3.7b and 3.10b assume that the time required for the I/O operation is
relatively short: less than the time to complete the execution of instructions between write
operations in the user program. In this case, the segment of code labeled code segment
2 is interrupted. A portion of the code (2a) executes (while the I/O operation is performed)
and then the interrupt occurs (upon the completion of the I/O operation). After
the interrupt is serviced, execution resumes with the remainder of code segment 2 (2b).

## Slide 20: Program Timing: Long I/O Wait
Notes: The more typical case, especially for a slow device such as a printer, is that the
I/O operation will take much more time than executing a sequence of user instructions.
Figure 3.7c indicates this state of affairs. In this case, the user program reaches
the second WRITE call before the I/O operation spawned by the first call is complete.
The result is that the user program is hung up at that point. When the preceding
I/O operation is completed, this new WRITE call may be processed, and a new
I/O operation may be started. Figure 3.11 shows the timing for this situation with
and without the use of interrupts. We can see that there is still a gain in efficiency
because part of the time during which the I/O operation is under way overlaps with
the execution of user instructions.

## Slide 21: Instruction Cycle State Diagram With Interrupts
Notes: Figure 3.12 shows a revised instruction cycle state diagram that includes
interrupt cycle processing.

## Slide 22: Multiple Interrupts
Transfer of
Control
Notes: Two approaches can be taken to dealing with multiple interrupts. The first is to
disable interrupts while an interrupt is being processed. A disabled interrupt simply
means that the processor can and will ignore that interrupt request signal. If an interrupt
occurs during this time, it generally remains pending and will be checked by
the processor after the processor has enabled interrupts. Thus, when a user program
is executing and an interrupt occurs, interrupts are disabled immediately. After the
interrupt handler routine completes, interrupts are enabled before resuming the
user program, and the processor checks to see if additional interrupts have occurred.
This approach is nice and simple, as interrupts are handled in strict sequential order
(Figure 3.13a).
The drawback to the preceding approach is that it does not take into account
relative priority or time-critical needs. For example, when input arrives from the
communications line, it may need to be absorbed rapidly to make room for more
input. If the first batch of input has not been processed before the second batch
arrives, data may be lost.
A second approach is to define priorities for interrupts and to allow an
interrupt of higher priority to cause a lower-priority interrupt handler to be itself
interrupted (Figure 3.13b).

## Slide 23: Time Sequence of Multiple Interrupts
Example
Notes: As an example of this second approach, consider a
system with three I/O devices: a printer, a disk, and a communications line, with
increasing priorities of 2, 4, and 5, respectively. Figure 3.14 illustrates a possible
sequence. A user program begins at t = 0. At t = 10, a printer interrupt occurs; user
information is placed on the system stack and execution continues at the printer
interrupt service routine (ISR). While this routine is still executing, at t = 15, a
communications interrupt occurs. Because the communications line has higher
priority than the printer, the interrupt is honored. The printer ISR is interrupted,
its state is pushed onto the stack, and execution
continues at the communications ISR. While this routine is executing, a disk interrupt occurs (t = 20). Because this interrupt is of lower priority, it is simply held, and the communications ISR runs
to completion.
When the communications ISR is complete (t = 25), the previous processor
state is restored, which is the execution of the printer ISR. However, before even a
single instruction in that routine can be executed, the processor honors the higher priority
disk interrupt and control transfers to the disk ISR. Only when that routine
is complete
(t = 35) is the printer ISR resumed. When that routine completes (t = 40),
control finally returns to the user program.

## Slide 24: I/O Function
I/O module can exchange data directly with the processor
Processor can read data from or write data to an I/O module
  Processor identifies a specific device that is controlled by a particular I/O module
  I/O instructions rather than memory referencing instructions
In some cases it is desirable to allow I/O exchanges to occur directly with memory
  The processor grants to an I/O module the authority to read from or write to memory so that the I/O memory transfer can occur without tying up the processor
  The I/O module issues read or write commands to memory relieving (làm giảm nhẹ) the processor of responsibility for the exchange
  This operation is known as direct memory access (DMA)
Notes: An I/O module (e.g., a disk controller) can exchange data directly with the
processor. Just as the processor can initiate a read or write with memory, designating
the address of a specific location, the processor can also read data from or write data
to an I/O module. In this latter case, the processor identifies a specific device that is
controlled by a particular I/O module. Thus, an instruction sequence similar in form to
that of Figure 3.5 could occur, with I/O instructions rather than memory-referencing
instructions.
In some cases, it is desirable to allow I/O exchanges to occur directly with
memory. In such a case, the processor grants to an I/O module the authority to read
from or write to memory, so that the I/O-memory transfer can occur without tying up
the processor. During such a transfer, the I/O module issues read or write commands
to memory, relieving the processor of responsibility for the exchange. This operation
is known as direct memory access (DMA) and is examined in Chapter 7.

## Slide 25: 3.3- Interconne_ ction Structures
Notes: A computer consists of a set of components or modules of three basic types
(processor, memory, I/O) that communicate with each other. In effect, a computer is
a network of basic modules. Thus, there must be paths for connecting the modules.
The collection of paths connecting the various modules is called the interconnection
structure. The design of this structure will depend on the exchanges that
must be made among modules.
Figure 3.15 suggests the types of exchanges that are needed by indicating the
major forms of input and output for each module type:
• Memory: Typically, a memory module will consist of N words of equal length.
Each word is assigned a unique numerical address (0, 1, …, N - 1). A word of
data can be read from or written into the memory. The nature of the operation
is indicated by read and write control signals. The location for the operation is
specified by an address.
• I/O module: From an internal (to the computer system) point of view, I/O
is functionally similar to memory. There are two operations, read and write.
Further, an I/O module may control more than one external device. We can
refer to each of the interfaces to an external device as a port and give each
a unique address (e.g., 0, 1, …, M - 1). In addition, there are external data
paths for the input and output of data with an external device. Finally, an I/O
module may be able to send interrupt signals to the processor.
• Processor: The processor reads in instructions and data, writes out data after
processing, and uses control signals to control the overall operation of the
system. It also receives interrupt signals.

## Slide 26: The interconnection structure must support the following types of transfers:
Memory to processor
Processor reads an instruction or a unit of data from memory
Processor to memory
Processor writes a unit of data to memory
I/O to processor
Processor reads data from an I/O device via an I/O module
Processor to I/O
Processor sends data to the I/O device
I/O to or from memory
An I/O module is allowed to exchange data directly with memory without going through the processor using direct memory access
Notes: The preceding list defines the data to be exchanged. The interconnection
structure must support the following types of transfers:
• Memory to processor: The processor reads an instruction or a unit of data
from memory.
• Processor to memory: The processor writes a unit of data to memory.
• I/O to processor: The processor reads data from an I/O device via an I/O
module.
• Processor to I/O: The processor sends data to the I/O device.
• I/O to or from memory: For these two cases, an I/O module is allowed to exchange
data directly with memory, without going through the processor, using
direct memory access.
Over the years, a number of interconnection structures have been tried. By
far the most common are (1) the bus and various multiple-bus structures, and (2)
point-to-point interconnection structures with packetized data transfer. We devote
the remainder of this chapter for a discussion of these structures.

## Slide 27: 3.4-Bus Inter-connection
A communication pathway connecting two or more devices
Key characteristic is that it is a shared transmission medium
Signals transmitted by any one device are available for reception by all other devices attached to the bus
If two devices transmit during the same time period their signals will overlap and become garbled
Typically consists of multiple communication lines
Each line is capable of transmitting signals representing binary 1 and binary 0
Computer systems contain a number of different buses that provide pathways between components at various levels of the computer system hierarchy
System bus
A bus that connects major computer components (processor, memory, I/O)
The most common computer interconnection structures are based on the use of one or more system buses
Notes: A bus is a communication pathway connecting two or more devices. A key characteristic
of a bus is that it is a shared transmission medium. Multiple devices connect
to the bus, and a signal transmitted by any one device is available for reception by
all other devices attached to the bus. If two devices transmit during the same time
period, their signals will overlap and become garbled. Thus, only one device at a
time can successfully transmit.
Typically, a bus consists of multiple communication pathways, or lines. Each
line is capable of transmitting signals representing binary 1 and binary 0. Over time,
a sequence of binary digits can be transmitted across a single line. Taken together,
several lines of a bus can be used to transmit binary digits simultaneously (in parallel).
For example, an 8-bit unit of data can be transmitted over eight bus lines.
Computer systems contain a number of different buses that provide pathways
between components at various levels of the computer system hierarchy. A bus that
connects major computer components (processor, memory, I/O) is called a system
bus. The most common computer interconnection structures are based on the use of
one or more system buses.

## Slide 28: Data Bus
Data lines that provide a path for moving data among system modules
May consist of 32, 64, 128, or more separate lines
The number of lines is referred to as the width of the data bus
The number of lines determines how many bits can be transferred at a time
The width of the data bus
is a key factor in
determining overall
system performance
Notes: A system bus consists, typically, of from about fifty to hundreds of separate lines.
The data lines provide a path for moving data among system modules. These
lines, collectively, are called the data bus. The data bus may consist of 32, 64, 128, or
even more separate lines, the number of lines being referred to as the width of the
data bus. Because each line can carry only 1 bit at a time, the number of lines determines
how many bits can be transferred at a time. The width of the data bus is a key
factor in determining overall system performance. For example, if the data bus is
32 bits wide and each instruction is 64 bits long, then the processor must access the
memory module twice during each instruction cycle.

## Slide 29: Address Bus Control Bus
Used to designate the source or destination of the data on the data bus
  If the processor wishes to read a word of data from memory it puts the address of the desired word on the address lines
Width determines the maximum possible memory capacity of the system
Also used to address I/O ports
  The higher order bits are used to select a particular module on the bus and the lower order bits select a memory location or I/O port within the module
Used to control the accessand the use of the data and address lines
Because the data and address lines are shared by all components there must be a means of controlling their use
Control signals transmit both command and timing information among system modules
Timing signals indicate the validity of data and address information
Command signals specify operations to be performed
Notes: The address lines are used to designate the source or destination of the data on
the data bus. For example, if the processor wishes to read a word (8, 16, or 32 bits)
of data from memory, it puts the address of the desired word on the address lines.
Clearly, the width of the address bus determines the maximum possible memory
capacity of the system. Furthermore, the address lines are generally also used to
address I/O ports. Typically, the higher-order bits are used to select a particular
module on the bus, and the lower-order bits select a memory location or I/O port
within the module. For example, on an 8-bit address bus, address 01111111 and
below might reference locations in a memory module (module 0) with 128 words
of memory, and address 10000000 and above refer to devices attached to an I/O
module (module 1).
The control lines are used to control the access to and the use of the data and
address lines. Because the data and address lines are shared by all components,
there must be a means of controlling their use. Control signals transmit both command
and timing information among system modules. Timing signals indicate the
validity of data and address information. Command signals specify operations to be
performed. Typical control lines include:
• Memory write: causes data on the bus to be written into the addressed location
• Memory read: causes data from the addressed location to be placed on the
bus
• I/O write: causes data on the bus to be output to the addressed I/O port
• I/O read: causes data from the addressed I/O port to be placed on the bus
• Transfer ACK: indicates that data have been accepted from or placed on the
bus
• Bus request: indicates that a module needs to gain control of the bus
• Bus grant: indicates that a requesting module has been granted control of the
bus
• Interrupt request: indicates that an interrupt is pending
• Interrupt ACK: acknowledges that the pending interrupt has been recognized
• Clock: is used to synchronize operations
• Reset: initializes all modules

## Slide 30: Bus Interconnection Scheme
Notes: The operation of the bus is as follows. If one module wishes to send data to
another, it must do two things: (1) obtain the use of the bus, and (2) transfer data
via the bus. If one module wishes to request data from another module, it must (1)
obtain the use of the bus, and (2) transfer a request to the other module over the
appropriate control and address lines. It must then wait for that second module to
send the data.

## Slide 31
Fig. 3.17- Example Bus Configuration
Notes: If a great number of devices are connected to the bus, performance will suffer.
There are two main causes:
1. In general, the more devices attached to the bus, the greater the bus length
and hence the greater the propagation delay. This delay determines the time
it takes for devices to coordinate the use of the bus. When control of the bus
passes from one device to another frequently, these propagation delays can
noticeably affect performance.
2. The bus may become a bottleneck as the aggregate data transfer demand
approaches the capacity of the bus. This problem can be countered to some
extent by increasing the data rate that the bus can carry and by using wider
buses (e.g., increasing the data bus from 32 to 64 bits). However, because the
data rates generated by attached devices (e.g., graphics and video controllers,
network interfaces) are growing rapidly, this is a race that a single bus is
ultimately destined to lose.
Accordingly, most bus-based computer systems use multiple buses, generally
laid out in a hierarchy. A typical traditional structure is shown in Figure 3.17a. There
is a local bus that connects the processor to a cache memory and that may support
one or more local devices. The cache memory controller connects the cache not only
to this local bus, but to a system bus to which are attached all of the main memory
modules. In contemporary systems, the cache is in the same chip as the processor, and
so an external bus or other interconnect scheme is not needed, although there may
also be an external cache. As will be discussed in Chapter 4, the use of a cache structure
insulates the processor from a requirement to access main memory frequently.
Hence, main memory can be moved off of the local bus onto a system bus. In this way,
I/O transfers to and from the main memory across the system bus do not interfere
with the processor’s activity.
It is possible to connect I/O controllers directly onto the system bus. A more
efficient solution is to make use of one or more expansion buses for this purpose.
An expansion bus interface buffers data transfers between the system bus and the
I/O controllers on the expansion bus. This arrangement allows the system to support
a wide variety of I/O devices and at the same time insulate memory-to-processor
traffic from I/O traffic.
Figure 3.17a shows some typical examples of I/O devices that might be attached
to the expansion bus. Network connections include local area networks (LANs)
such as a 10-Mbps Ethernet and connections to wide area networks (WANs) such as
a packet-switching network. SCSI (small computer system interface) is itself a type
of bus used to support local disk drives and other peripherals. A serial port could be
used to support a printer or scanner.
This traditional bus architecture is reasonably efficient but begins to break
down as higher and higher performance is seen in the I/O devices. In response to
these growing demands, a common approach taken by industry is to build a high-speed
bus that is closely integrated with the rest of the system, requiring only a
bridge between the processor’s bus and the high-speed bus. This arrangement is
sometimes known as a mezzanine architecture.
Figure 3.17b shows a typical realization of this approach. Again, there is a local
bus that connects the processor to a cache controller, which is in turn connected to
a system bus that supports main memory. The cache controller is integrated into a
bridge, or buffering device, that connects to the high-speed bus. This bus supports
connections to high-speed LANs, such as Fast Ethernet at 100 Mbps, video and
graphics workstation controllers, as well as interface controllers to local peripheral
buses, including SCSI and FireWire. The latter is a high-speed bus arrangement
specifically designed to support high-capacity I/O devices. Lower-speed devices are
still supported off an expansion bus, with an interface buffering traffic between the
expansion bus and the high-speed bus.
The advantage of this arrangement is that the high-speed bus brings high demand
devices into closer integration with the processor and at the same time is
independent of the processor. Thus, differences in processor and high-speed bus
speeds and signal line definitions are tolerated. Changes in processor architecture
do not affect the high-speed bus, and vice versa.

## Slide 32
Fig. 3.17- Example Bus Configuration
Notes: If a great number of devices are connected to the bus, performance will suffer.
There are two main causes:
1. In general, the more devices attached to the bus, the greater the bus length
and hence the greater the propagation delay. This delay determines the time
it takes for devices to coordinate the use of the bus. When control of the bus
passes from one device to another frequently, these propagation delays can
noticeably affect performance.
2. The bus may become a bottleneck as the aggregate data transfer demand
approaches the capacity of the bus. This problem can be countered to some
extent by increasing the data rate that the bus can carry and by using wider
buses (e.g., increasing the data bus from 32 to 64 bits). However, because the
data rates generated by attached devices (e.g., graphics and video controllers,
network interfaces) are growing rapidly, this is a race that a single bus is
ultimately destined to lose.
Accordingly, most bus-based computer systems use multiple buses, generally
laid out in a hierarchy. A typical traditional structure is shown in Figure 3.17a. There
is a local bus that connects the processor to a cache memory and that may support
one or more local devices. The cache memory controller connects the cache not only
to this local bus, but to a system bus to which are attached all of the main memory
modules. In contemporary systems, the cache is in the same chip as the processor, and
so an external bus or other interconnect scheme is not needed, although there may
also be an external cache. As will be discussed in Chapter 4, the use of a cache structure
insulates the processor from a requirement to access main memory frequently.
Hence, main memory can be moved off of the local bus onto a system bus. In this way,
I/O transfers to and from the main memory across the system bus do not interfere
with the processor’s activity.
It is possible to connect I/O controllers directly onto the system bus. A more
efficient solution is to make use of one or more expansion buses for this purpose.
An expansion bus interface buffers data transfers between the system bus and the
I/O controllers on the expansion bus. This arrangement allows the system to support
a wide variety of I/O devices and at the same time insulate memory-to-processor
traffic from I/O traffic.
Figure 3.17a shows some typical examples of I/O devices that might be attached
to the expansion bus. Network connections include local area networks (LANs)
such as a 10-Mbps Ethernet and connections to wide area networks (WANs) such as
a packet-switching network. SCSI (small computer system interface) is itself a type
of bus used to support local disk drives and other peripherals. A serial port could be
used to support a printer or scanner.
This traditional bus architecture is reasonably efficient but begins to break
down as higher and higher performance is seen in the I/O devices. In response to
these growing demands, a common approach taken by industry is to build a high-speed
bus that is closely integrated with the rest of the system, requiring only a
bridge between the processor’s bus and the high-speed bus. This arrangement is
sometimes known as a mezzanine architecture.
Figure 3.17b shows a typical realization of this approach. Again, there is a local
bus that connects the processor to a cache controller, which is in turn connected to
a system bus that supports main memory. The cache controller is integrated into a
bridge, or buffering device, that connects to the high-speed bus. This bus supports
connections to high-speed LANs, such as Fast Ethernet at 100 Mbps, video and
graphics workstation controllers, as well as interface controllers to local peripheral
buses, including SCSI and FireWire. The latter is a high-speed bus arrangement
specifically designed to support high-capacity I/O devices. Lower-speed devices are
still supported off an expansion bus, with an interface buffering traffic between the
expansion bus and the high-speed bus.
The advantage of this arrangement is that the high-speed bus brings high demand
devices into closer integration with the processor and at the same time is
independent of the processor. Thus, differences in processor and high-speed bus
speeds and signal line definitions are tolerated. Changes in processor architecture
do not affect the high-speed bus, and vice versa.

## Slide 33: Elements of Bus Design
Dedicated: chuyên dụng, multiplex: đa thành phần
Synchronous- đồng bộ- At a time, only one device can uses the bus. The others must wait until the bus is idle.
Arbitration: phân xử, quản lý
Asynchronous- không đồng bộ- At a time, some devices can use the bus concurrently
Notes: Although a variety of different bus implementations exist, there are a few basic
parameters or design elements that serve to classify and differentiate buses. Table 3.2
lists key elements.
Bus Types: Bus lines can be separated into two generic types: dedicated and
multiplexed. A dedicated bus line is permanently assigned either to one function or
to a physical subset of computer components.
An example of functional dedication is the use of separate dedicated address
and data lines, which is common on many buses. However, it is not essential. For
example, address and data information may be transmitted over the same set of
lines using an Address Valid control line. At the beginning of a data transfer, the
address is placed on the bus and the Address Valid line is activated. At this point,
each module has a specified period of time to copy the address and determine if
it is the addressed module. The address is then removed from the bus, and the
same bus connections are used for the subsequent read or write data transfer. This
method of using the same lines for multiple purposes is known as time multiplexing.
The advantage of time multiplexing is the use of fewer lines, which saves space
and, usually, cost. The disadvantage is that more complex circuitry is needed within
each module. Also, there is a potential reduction in performance because certain
events that share the same lines cannot take place in parallel.
Physical dedication refers to the use of multiple buses, each of which connects
only a subset of modules. A typical example is the use of an I/O bus to interconnect
all I/O modules; this bus is then connected to the main bus through some type of I/O
adapter module. The potential advantage of physical dedication is high throughput,
because there is less bus contention. A disadvantage is the increased size and cost of
the system.
Method of arbitration: In all but the simplest systems, more than one module
may need control of the bus. For example, an I/O module may need to read or write
directly to memory, without sending the data to the processor. Because only one unit
at a time can successfully transmit over the bus, some method of arbitration is needed.
The various methods can be roughly classified as being either centralized arbitration
or distributed arbitration. In a centralized scheme, a single hardware device, referred
to as a bus controller or arbiter, is responsible for allocating time on the bus. The
device may be a separate module or part of the processor. In a distributed scheme,
there is no central controller. Rather, each module contains access control logic and
the modules act together to share the bus. With both methods of arbitration, the
purpose is to designate one device, either the processor or an I/O module, as master.
The master may then initiate a data transfer (e.g., read or write) with some other
device, which acts as slave for this particular exchange.
Timing: Timing refers to the way in which events are coordinated on the bus. Buses
use either synchronous timing or asynchronous timing.

## Slide 34: Timing of Synchronous Bus Operations
Notes: With synchronous timing, the occurrence of events on the bus is determined
by a clock. The bus includes a clock line upon which a clock transmits a regular
sequence of alternating 1s and 0s of equal duration. A single 1–0 transmission is
referred to as a clock cycle or bus cycle and defines a time slot. All other devices on
the bus can read the clock line, and all events start at the beginning of a clock cycle.
Figure 3.18 shows a typical, but simplified, timing diagram for synchronous read
and write operations (see Appendix N for a description of timing diagrams). Other
bus signals may change at the leading edge of the clock signal (with a slight reaction
delay). Most events occupy a single clock cycle. In this simple example, the processor
places a memory address on the address lines during the first clock cycle and
may assert various status lines. Once the address lines have stabilized, the processor
issues an address enable signal. For a read operation, the processor issues a read
command at the start of the second cycle. A memory module recognizes the address
and, after a delay of one cycle, places the data on the data lines. The processor reads
the data from the data lines and drops the read signal. For a write operation, the
processor puts the data on the data lines at the start of the second cycle and issues a
write command after the data lines have stabilized. The memory module copies the
information from the data lines during the third clock cycle.

## Slide 35: Timing of Asynchronous Bus Operations
Notes: With asynchronous timing, the occurrence of one event on a bus follows
and depends on the occurrence of a previous event. In the simple read example of
Figure 3.19a, the processor places address and status signals on the bus. After pausing
for these signals to stabilize, it issues a read command, indicating the presence
of valid address and control signals. The appropriate memory decodes the address and
responds by placing the data on the data line. Once the data lines have stabilized,
the memory module asserts the acknowledged line to signal the processor that the
data are available. Once the master has read the data from the data lines, it deasserts
the read signal. This causes the memory module to drop the data and acknowledge
lines. Finally, once the acknowledge line is dropped, the master removes the
address information.
Figure 3.19b shows a simple asynchronous write operation. In this case, the
master places the data on the data line at the same time that it puts signals on the
status and address lines. The memory module responds to the write command by
copying the data from the data lines and then asserting the acknowledge line. The
master then drops the write signal and the memory module drops the acknowledge
signal.
Synchronous timing is simpler to implement and test. However, it is less
flexible than asynchronous timing. Because all devices on a synchronous bus are
tied to a fixed clock rate, the system cannot take advantage of advances in device
performance. With asynchronous timing, a mixture of slow and fast devices, using
older and newer technology, can share a bus.

## Slide 36: Questions (Write answers to your notebook)
3.1 What general categories of functions are specified by computer instructions?
3.2 List and briefly define the possible states that define an instruction execution.
3.3 List and briefly define two approaches to dealing with multiple interrupts.
3.4 What types of transfers must a computer’s interconnection structure (e.g., bus) support?
3.5 What is the benefit of using a multiple-bus architecture compared to a single-bus architecture?
Notes: The shared bus architecture was the standard approach to interconnection between
the processor and other components (memory, I/O, and so on) for decades. But
contemporary systems increasingly rely on point-to-point interconnection rather
than shared buses.
The principal reason driving the change from bus to point-to-point interconnect
was the electrical constraints encountered with increasing the frequency of wide
synchronous buses. At higher and higher data rates, it becomes increasingly difficult
to perform the synchronization and arbitration functions in a timely fashion. Further,
with the advent of multi-core chips, with multiple processors and significant memory
on a single chip, it was found that the use of a conventional shared bus on the same
chip magnified the difficulties of increasing bus data rate and reducing bus latency
to keep up interconnect has lower latency, higher data rate, and better scalability.

## Slide 37: Building Block Read by yourself
3.5- Point-to-Point Interconnect
3.6- PCI Express
Notes: The shared bus architecture was the standard approach to interconnection between
the processor and other components (memory, I/O, and so on) for decades. But
contemporary systems increasingly rely on point-to-point interconnection rather
than shared buses.
The principal reason driving the change from bus to point-to-point interconnect
was the electrical constraints encountered with increasing the frequency of wide
synchronous buses. At higher and higher data rates, it becomes increasingly difficult
to perform the synchronization and arbitration functions in a timely fashion. Further,
with the advent of multi-core chips, with multiple processors and significant memory
on a single chip, it was found that the use of a conventional shared bus on the same
chip magnified the difficulties of increasing bus data rate and reducing bus latency
to keep up interconnect has lower latency, higher data rate, and better scalability.

## Slide 38: Summary
Computer components
Computer function
  Instruction fetch and execute
  Interrupts
  I/O function
Interconnection structures
Bus interconnection
  Bus structure
  Multiple bus hierarchies
  Elements of bus design
Chapter 3
A Top-Level View of Computer Function and Interconnection
Notes: Chapter 3 summary.